## Slide 1
To adjust the compensation to make amplifier stable for a desired load, change C82 and C83 (0805 size surface mount components)
Optional (if circuit still is not stable): Short circuit across the parallel RC circuit formed by R190 and C127
If more than 3.5 amps output current is needed, replaced R152 and R166 with a smaller current limiter resistor. To get full 8 amp output, use 0 ohms. See OPA549 datasheet for details.
If you want to slow down or speed up the rise time of the output current, you can change C84.
One example output channel’s analog stage: